## Slide 1: IP Routing Basics

## Slide 2
There are typically multiple IP subnets on a typical data communication network. Layer 3 devices are required to exchange data between these IP subnets. These devices have the routing capability and can forward data across subnets.
Routing is the basic element of data communication networks. It is the process of selecting paths on a network along which packets are sent from a source to a destination.
This course introduces the basic concepts of routing.

## Slide 3
On completion of this course, you will be able to:
  Understand the basic principles of routers.
  Know how routers select optimal routes.
  Understand the contents of routing tables.
  Master advanced routing features.

## Slide 4
Overview of IP Routing
  Basic Concepts of Routing
  Generation of Routing Entries
  Optimal Route Selection
  Route-based Forwarding
Static Routing
Dynamic Routing
Advanced Routing Features

## Slide 5: Background: Inter-Subnet Communication
N
M
How to communicate with the network M?
An IP address uniquely identifies a node on a network. Each IP address belongs to a unique subnet, and each subnet may belong to a different area of the network.
To implement IP addressing, subnets in different areas need to communicate with each other.
Notes: A unique network node can be found based on a specific IP address. Each IP address belongs to a unique subnet. These subnets may be distributed around the world and constitute a global network.
To implement communication between different subnets, network devices need to forward IP packets from different subnets to their destination IP subnets.

## Slide 6: Routes
Routes are the path information used to guide packet forwarding.
A routing device is a network device that forwards packets to a destination subnet based on routes. The most common routing device is a router.
A routing device maintains an IP routing table that stores routing information.
R1
R2
R3
N
M
R4
Data
Route-based Packet Forwarding
Destination-based forwarding
Router
Gateway
Gateway
Notes: A gateway and an intermediate node (a router) select a proper path according to the destination address of a received IP packet, and forward the packet to the next router. The last-hop router on the path performs Layer 2 addressing and forwards the packet to the destination host. This process is called route-based forwarding.
The intermediate node selects the best path from its IP routing table to forward packets.
A routing entry contains a specific outbound interface and next hop, which are used to forward IP packets to the corresponding next-hop device.

## Slide 7: Routing Information
A route contains the following information:
  Destination: identifies a destination subnet.
  Mask: identifies a subnet together with a destination IP address.
  Outbound interface: indicates the interface through which a data packet is sent out of the local router.
  Next hop: indicates the next-hop address used by the router to forward the data packet to the destination subnet.
  The information identifies the destination subnet and specifies the path for forwarding data packets.
10.1.1.0/24
1.1.1.2
GE0/0/0
1.1.1.3
IP routing table
Destination/Mask | Outbound Interface | Next Hop
10.1.1.0/24 | GE0/0/0 | 1.1.1.2
Notes: Based on the information contained in a route, a router can forward IP packets to the destination along the required path.
The destination address and mask identify the destination address of an IP packet. After an IP packet matches a specific route, the router determines the forwarding path according to the outbound interface and next hop of the route.
The next-hop device for forwarding the IP packet cannot be determined based only on the outbound interface. Therefore, the next-hop device address must be specified.

## Slide 8: IP Routing Table
R2
R4
GE0/0
2.2.2.1/30
R1
2.2.2.2/30
R3
3.3.3.2/30
GE0/1
3.3.3.1/30
GE0/2
1.1.1.1/30
1.1.1.2/30
Destination/Mask | Next Hop | Outbound Interface
11.0.0.0/8 | 2.2.2.2 | GE0/0
13.0.0.0/8 | 3.3.3.2 | GE0/1
14.0.0.0/8 | 1.1.1.2 | GE0/2
… |  | 
1.1.1.0/30 | 1.1.1.1 | GE0/2
1.1.1.1/32 | 127.0.0.1 | GE0/2
Routers discover routes using multiple methods.
A router selects the optimal route and installs it in its IP routing table.
The router forwards IP packets based on routes in the IP routing table.
Routers manage path information by managing their IP routing tables.
14.0.0.0/8
11.0.0.0/8
13.0.0.0/8
Notes: A router forwards packets based on its IP routing table.
An IP routing table contains many routing entries.
An IP routing table contains only optimal routes but not all routes.
A router manages routing information by managing the routing entries in its IP routing table.

## Slide 9
Overview of IP Routing
  Basic Concepts of Routing
  Generation of Routing Entries
  Optimal Route Selection
  Route-based Forwarding
Static Routing
Dynamic Routing
Advanced Routing Features

## Slide 10: How to Obtain Routing Information
A router forwards packets based on its IP routing table. To implement route-based packet forwarding, the router needs to obtain routes. The following describes the common methods of obtaining routes.
GE0/0/0
10.1.1.0/24
20.1.1.0/24
GE0/0/1
GE0/0/1
30.1.1.0/24
40.1.1.0/24
GE0/0/2
Direct Routes
Protocol | Destination/Mask | Outbound Interface
Direct | 10.1.1.0/24 | GE0/0/0
Direct | 20.1.1.0/24 | GE0/0/1
Static Routes
Dynamic Routes
Protocol | Destination/Mask | Outbound Interface
Static | 30.1.1.0/24 | GE0/0/1
Dynamic routing protocol
OSPF
Protocol | Destination/Mask | Outbound Interface
OSPF | 40.1.1.0/24 | GE0/0/2
Direct routes are automatically generated by devices and point to local directly connected networks.
Static routes are manually configured by network administrators.
Dynamic routes are learned by dynamic routing protocols running on routers.
Notes: Direct routes are the routes destined for the subnets to which directly connected interfaces belong. They are automatically generated by devices.
Static routes are manually configured by network administrators.
Dynamic routes are learned by dynamic routing protocols, such as OSPF, IS-IS, and BGP.

## Slide 11: Direct Routes (1)
GE0/0/1
20.1.1.2/24
GE0/0/0
10.0.0.2/24
RTB
A direct route is automatically generated by a device and points to a local directly-connected network.
When a router is the last hop router, IP packets to be forwarded will match a direct route and the router will directly forward the IP packet to the destination host.
When a direct route is used for packet forwarding, the destination IP address of a packet to be forwarded and the IP address of the router‘s outbound interface are in the same subnet.
Direct routes in the IP routing table of RTB
Destination/Mask | Protocol | Next Hop | Outbound Interface
10.0.0.0/24 | Direct | 10.0.0.2 | GE0/0/0
20.1.1.0/24 | Direct | 20.1.1.2 | GE0/0/1
Direct Routes
10.0.0.0/24
20.1.1.0/24
Notes: When a packet matches a direct route, a router checks its ARP entries and forwards the packet to the destination address based on the ARP entry for this destination address. In this case, the router is the last hop router.
The next-hop address of a direct route is not an interface address of another device. The destination subnet of the direct route is the subnet to which the local outbound interface belongs. The local outbound interface is the last hop interface and does not need to forward the packet to any other next hop. Therefore, the next-hop address of a direct route in the IP routing table is the address of the local outbound interface.
When a router forwards packets using a direct route, it does not deliver packets to the next hop. Instead, the router checks its ARP entries and forwards packets to the destination IP address based on the required ARP entry.

## Slide 12: Direct Routes (2)
Direct routes in the IP routing table of RTB
GE0/0/1
20.1.1.2/24
GE0/0/0
10.0.0.2/24
GE0/0/1
20.1.1.3/24
GE0/0/0
10.0.0.1/24
RTA
RTC
RTB
Destination/Mask | Protocol | Next Hop | Outbound Interface
20.1.1.0/24 | Direct | 20.1.1.2 | G0/0/1
Direct routes
Not all the direct routes generated for interfaces are installed in the IP routing table. Only the direct routes of which the physical status and protocol status of interfaces are up are installed in the IP routing table.
When GE0/0/0 goes down, the direct route for this interface is not installed in the IP routing table.

## Slide 13
Overview of IP Routing
  Basic Concepts of Routing
  Generation of Routing Entries
  Optimal Route Selection
  Route-based Forwarding
Static Routing
Dynamic Routing
Advanced Routing Features

## Slide 14: Examining the IP Routing Table
<Quidway> display ip routing-table
Route Flags: R - relay, D - download to fib
------------------------------------------------------------------------------------------------------Routing Tables: Public
Destinations : 6 Routes : 6
Destination/Mask Proto Pre Cost Flags NextHop Interface
1.1.1.1/32 Static 60 0 D 0.0.0.0 NULL0
2.2.2.2/32 Static 60 0 D 100.0.0.2 Vlanif100
100.0.0.0/24 Direct 0 0 D 100.0.0.1 Vlanif100
100.0.0.1/32 Direct 0 0 D 127.0.0.1 Vlanif100
127.0.0.0/8 Direct 0 0 D 127.0.0.1 InLoopBack0
127.0.0.1/32 Direct 0 0 D 127.0.0.1 InLoopBack0
Destination/Mask
Protocol
Route preference
Cost (Metric)
Flag
Next-hop address
Outbound interface

## Slide 15: Fields in the IP Routing Table
Destination/Mask: indicates the destination network address and mask of a specific route. The subnet address of a destination host or router is obtained through the AND operation on the destination address and mask. For example, if the destination address is 1.1.1.1 and the mask is 255.255.255.0, the IP address of the subnet to which the host or router belongs is 1.1.1.0.
Proto (Protocol): indicates the protocol type of the route, that is, the protocol through which a router learns the route.
Pre (Preference): indicates the routing protocol preference of the route. There may be multiple routes to the same destination, which have different next hops and outbound interfaces. These routes may be discovered by different routing protocols or be manually configured. A router selects the route with the highest preference (with the lowest preference value) as the optimal route.
Cost: indicates the cost of the route. When multiple routes to the same destination have the same preference, the route with the lowest cost is selected as the optimal route.
NextHop: indicates the local router’s next-hop address of the route to the destination network. This field specifies the next-hop device to which packets are forwarded.
Interface: indicates the outbound interface of the route. This field specifies the local interface through which the local router forwards packets.
Notes: The Preference field is used to compare routes from different routing protocols, while the Cost field is used to compare routes from the same routing protocol. In the industry, the cost is also known as the metric.

## Slide 16: Route Preference - Basic Concepts
When a router obtains routes to the same destination subnet from different routing protocols (these routes have the same destination network address and mask), the router compares the preferences of these routes and prefers the route with the lowest preference value.
A lower preference value indicates a higher preference.
The route with the highest preference is installed in the IP routing table.
Comparing Route Preferences
Same
Higher Preference
Destination subnet/mask
Routes
Preference
Installed in the IP routing table
Different

## Slide 17: Route Preference - Comparison Process
10.0.0.0/30
RTA
20.1.1.1/30
30.1.1.1/30
20.1.1.2/30
30.1.1.2/30
IP routing table of RTA
Dynamic routing protocol
OSPF
Comparing Route Preferences
Destination/Mask | Protocol | Preference | Next Hop
10.0.0.0/30 | Static | 60 | 30.1.1.2
10.0.0.0/30 | OSPF | 10 | 20.1.1.2
RTA discovers two routes to 10.0.0.0/30, one is an OSPF route and the other a static route. In this case, RTA compares the preferences of the two routes and selects the route with the lowest preference value.
Each routing protocol has a unique preference.
OSPF has a higher preference. Therefore, the OSPF route is installed in the IP routing table.
Installed in the IP routing table
Notes: RTA learns two routes to the same destination, one is a static route and the other an OSPF route. It then compares the preferences of the two routes, and prefers the OSPF route because this route has a higher preference. RTA installs the OSPF route in the IP routing table.

## Slide 18: Metric - Comparison Process
Dynamic routing protocol
OSPF
10.0.0.0/30
RTA
20.1.1.1/30
30.1.1.1/30
20.1.1.2/30
30.1.1.2/30
IP routing table of RTA
Cost=10
Cost=10
Cost=10
Metric comparison
Destination/Mask | Protocol | Cost | Next Hop
10.0.0.0/30 | OSPF | 20 | 20.1.1.2
10.0.0.0/30 | OSPF | 10 | 30.1.1.2
RTA learns two routes with the same destination address (10.0.0.0/30) and preference through OSPF. In this case, RTA needs to compare the metrics of the two routes.
The two routes have different metrics. The OSPF route with the next hop being 30.1.1.2 has a lower metric (with the cost 10), so it is installed in the IP routing table.
Installed in the IP routing table

## Slide 19: Route Preference - Common Default Values
The following table lists the default preference values of common route types:
Protocol | Route Type | Default Preference
Direct | Direct route | 0
Static | Static route | 60
Dynamic routing protocol | OSPF internal route | 10
 | OSPF external route | 150
Notes: The table lists the preferences of some common routing protocols. Actually, there are multiple types of dynamic routes. We will learn these routes in subsequent courses.

## Slide 20: Metric - Basic Concepts
When a router discovers multiple routes to the same destination network through the same routing protocol, the router selects the optimal route based on the metrics of these routes if these routes have the same preference.
The metric of a route indicates the cost of reaching the destination address of the route.
Common metrics include the hop count, bandwidth, delay, cost, load, and reliability.
The route with the lowest metric is installed in the IP routing table.
The metric is also known as the cost.
Comparing Metrics
Same
Higher preference
Routes
Preference
Installed in the IP routing table
Different
Metric
Same preference
Lower metric
Destination/mask

## Slide 21
Overview of IP Routing
  Basic Concepts of Routing
  Generation of Routing Entries
  Optimal Route Selection
  Route-based Forwarding
Static Routing
Dynamic Routing
Advanced Routing Features

## Slide 22: Longest Matching
When a router receives an IP packet, it compares the destination IP address of the packet with all routing entries in the local routing table bit by bit until the longest matching entry is found. This is the longest matching mechanism.
Destination IP address
Bit-by-bit matching
172.16.2.0
255.255.255.0
Routing entry 2
Routing entry 3
172.16.0.0
255.255.0.0
Routing entry 1
172.16.1.0
255.255.255.0
172.
16.
0 0 0 0 0 0 1 0
0 0 0 0 0 0 0 1
172.
16.
0 0 0 0 0 0 0 1
x x x x x x x x
172.
16.
0 0 0 0 0 0 1 0
x x x x x x x x
172.
16.
x x x x x x x x
x x x x x x x x
Mismatch
Longest match
Not the longest match
172.16.2.1

## Slide 23: Example of Longest Matching (1)
10.1.1.2/30
20.1.1.2/30
30.1.1.2/30
DATA
RTA
Example of Longest Matching
IP routing table of RTA
Destination/Mask | Next Hop
192.168.0.0/16 | 10.1.1.2
192.168.2.0/24 | 20.1.1.2
192.168.3.0/24 | 30.1.1.2
There are two routes to 192.168.2.2 in the IP routing table of RTA, one has the 16-bit mask and the other has the 24-bit mask. According to the longest matching rule, the route with the 24-bit mask is preferred to guide the forwarding of packets destined for 192.168.2.2.
Match
Destination IP address:
192.168.2.2

## Slide 24: Example of Longest Matching (2)
According to the longest matching rule, only the route to 192.168.3.0/24 in the IP routing table matches the destination IP address 192.168.3.2. Therefore, this route is used to forward packets destined for 192.168.3.2.
10.1.1.2/30
20.1.1.2/30
30.1.1.2/30
RTA
Example of Longest Matching
IP routing table of RTA
Destination/Mask | Next Hop
192.168.0.0/16 | 10.1.1.2
192.168.2.0/24 | 20.1.1.2
192.168.3.0/24 | 30.1.1.2
Match
Data
Destination IP address:
192.168.3.2

## Slide 25: Route-based Forwarding Process
Gateway
Gateway
R1
R2
R3
GE0/1
GE0/1
20.0.1.2
20.0.1.1
30.0.1.1
30.0.1.2
GE0/0
GE0/0
GE0/0
GE0/1
Destination/Mask | Next Hop | Outbound Interface
10.0.1.0/24 | 10.0.1.1 | GE0/1
20.0.1.0/24 | 20.0.1.1 | GE0/0
30.0.1.0/24 | 20.0.1.2 | GE0/0
40.0.1.0/24 | 20.0.1.2 | GE0/0
Destination/Mask | Next Hop | Outbound Interface
20.0.1.0/24 | 20.0.1.2 | GE0/0
30.0.1.0/24 | 30.0.1.1 | GE0/1
10.0.1.0/24 | 20.0.1.1 | GE0/0
40.0.1.0/24 | 30.0.1.2 | GE0/1
Destination/Mask | Next Hop | Outbound Interface
40.0.1.0/24 | 40.0.1.1 | GE0/1
30.0.1.0/24 | 30.0.1.2 | GE0/0
10.0.1.0/24 | 30.0.1.1 | GE0/0
20.0.1.0/24 | 30.0.1.1 | GE0/0
10.0.1.0/24
40.0.1.0/24
30.0.1.0/24
20.0.1.0/24
10.0.1.1
40.0.1.1
Data
Destination IP address:
40.0.1.2
IP routing table of R3
IP routing table of R1
IP routing table of R2
Notes: The IP packets from 10.0.1.0/24 need to reach 40.0.1.0/24. After receiving these packets, the gateway R1 searches its IP routing table for the next hop and outbound interface and forwards the packets to R2. After the packets reach R2, R2 forwards the packets to R3 by searching its IP routing table. Upon receipt of the packets, R3 searches its IP routing table, finding that the destination IP address of the packets belongs to the subnet where a local interface resides. Therefore, R3 directly forwards the packets to the destination subnet 40.0.1.0/24.

## Slide 26: Summary of the IP Routing Table
When a router obtains routes to the same destination subnet with the same mask from different routing protocols, the router prefers the route with the lowest preference value of these routing protocols. If these routes are learned from the same routing protocol, the router prefers the route with the lowest cost. In summary, only the optimal route is installed in the IP routing table.
When a router receives a packet, it searches its IP routing table for the outbound interface and next hop based on the destination IP address of the packet. If it finds a matching routing entry, it forwards the packet according to the outbound interface and next hop specified by this entry. Otherwise, it discards the packet.
Packets are forwarded hop by hop. Therefore, all the routers along the path from the source to the destination must have routes destined for the destination. Otherwise, packet loss occurs.
Data communication is bidirectional. Therefore, both forward and backward routes must be available.

## Slide 27
Overview of IP Routing
Static Routing
Dynamic Routing
Advanced Routing Features

## Slide 28: Application Scenarios of Static Routes
GE0/0/1
20.1.1.2/24
GE0/0/0
10.0.0.2/24
GE0/0/1
20.1.1.3/24
GE0/0/0
10.0.0.1/24
RTA
RTC
RTB
Destined for 20.1.1.0/24
Destination | Protocol | Next Hop
20.1.1.0 | Static | 10.0.0.2
10.0.0.0 | Direct | 10.0.0.1
Static Routes
Static routes are manually configured by network administrators, have low system requirements, and apply to simple, stable, and small networks.
The disadvantage of static routes is that they cannot automatically adapt to network topology changes and so require manual intervention.
RTA needs to forward the packets with the destination address 20.1.1.0/24. However, the IP routing table of RTA has only one direct route, which does not match 20.1.1.0/24. In this case, a static route needs to be manually configured so that the packets sent from RTA to 20.1.1.0/24 can be forwarded to the next hop 10.0.0.2.

## Slide 29: Static Route Configuration
[Huawei] ip route-static ip-address { mask | mask-length } nexthop-address
Specify a next-hop IP address for a static route.
[Huawei] ip route-static ip-address { mask | mask-length } interface-type interface-number
Specify an outbound interface for a static route.
[Huawei] ip route-static ip-address { mask | mask-length } interface-type interface-number [ nexthop-address ]
Specify both the outbound interface and next hop for a static route.
When creating a static route, you can specify both the outbound interface and next hop. Alternatively, you can specify either the outbound interface or next hop, depending on the interface type:
For a point-to-point interface (such as a serial interface), you must specify the outbound interface.
For a broadcast interface (for example, an Ethernet interface) or a virtual template (VT) interface, you must specify the next hop.

## Slide 30: Configuration Example
S1/0/0
20.1.1.2/24
GE0/0/0
10.0.0.2/24
S1/0/0
20.1.1.3/24
GE0/0/0
10.0.0.1/24
RTA
RTC
RTB
Destined for 20.1.1.0/24
Destined for 10.1.1.0/24
[RTA] ip route-static 20.1.1.0 255.255.255.0 10.0.0.2
[RTC] ip route-static 10.0.0.0 255.255.255.0 S1/0/0
Configure RTA.
Configure RTC.
Configure static routes on RTA and RTC for communication between 10.0.0.0/24 and 20.1.1.0/24.
Packets are forwarded hop by hop. Therefore, all the routers along the path from the source to the destination must have routes destined for the destination.
Data communication is bidirectional. Therefore, both forward and backward routes must be available.

## Slide 31: Default Routes
Default routes are used only when packets to be forwarded do not match any routing entry in an IP routing table.
In an IP routing table, a default route is the route to network 0.0.0.0 (with the mask 0.0.0.0), namely, 0.0.0.0/0.
[RTA] ip route-static 0.0.0.0 0 10.0.0.2
RTA
RTB
192.168.1.0/24
10.0.0.2
10.0.0.1
192.168.2.0/24
.
GE0/0/0
GE0/0/0
192.168.254.0/24
192.168.3.0/24
.
RTA needs to forward packets to a subnet that is not directly connected to it and forwards the packets to 10.0.0.2.
10.0.0.0/24

## Slide 32: Application Scenarios of Default Routes
Enterprise network
Default routes are typically used at the egress of an enterprise network. For example, you can configure a default route on an egress device to enable the device to forward IP packets destined for any address on the Internet.
[RTA] ip route-static 0.0.0.0 0 1.2.3.254
1.2.3.0/24
RTA
GE0/0/0
1.2.3.4
PC
192.168.1.100
Gateway: 192.168.1.254
GE0/0/1
192.168.1.254
Internet
1.2.3.254

## Slide 33
Overview of IP Routing
Static Routing
Dynamic Routing
Advanced Routing Features

## Slide 34: Overview of Dynamic Routing
Dynamic routing protocols automatically discover and generate routes, and update routes when the topology changes. These protocols effectively reduce the workload of network administrators and are widely used on large networks.
Static routing
When the network scale expands, it becomes increasingly complex to manually configure static routes. In addition, when the network topology changes, static routes cannot adapt to these changes in a timely and flexible manner.
Dynamic routing OSPF
Static Routing
Dynamic Routing
To use static routes on any device, you must manually configure them.
Static routes cannot adapt to link changes.
Dynamic routes can be automatically discovered and learned.
Dynamic routes can adapt to topology changes.
Notes: The disadvantage of static routes is that they cannot automatically adapt to network topology changes and so require manual intervention.
Dynamic routing protocols provide different routing algorithms to adapt to network topology changes. Therefore, they are applicable to networks on which many Layer 3 devices are deployed.

## Slide 35: Classification of Dynamic Routing Protocols
Interior Gateway Protocol (IGP)
RIP
OSPF
IS-IS
Classification by the application scope
Exterior Gateway Protocol (EGP)
BGP
Classification by working mechanism and routing algorithm
Distance-vector routing protocol
Link-state routing protocol
OSPF
IS-IS
RIP
Notes: Dynamic routing protocols are classified into two types based on the routing algorithm:
  Distance-vector routing protocol
    RIP
  Link-state routing protocol
    OSPF
    IS-IS
  BGP uses a path vector algorithm, which is modified based on the distance-vector algorithm. Therefore, BGP is also called a path-vector routing protocol in some scenarios.
Dynamic routing protocols are classified into the following types by their application scope:
  IGPs run within an autonomous system (AS), including RIP, OSPF, and IS-IS.
  EGP runs between different ASs, among which BGP is the most frequently used.

## Slide 36
Overview of IP Routing
Static Routing
Dynamic Routing
Advanced Routing Features

## Slide 37: Route Recursion (1)
Route recursion is a recursive search process of the IP routing table where the next-hop IP address is wanted to route packets towards its destination but when found it is not part of any directly connected network.
Route Recursion
Equal-Cost Route
Floating Route
Route Summarization
GE0/0/1
20.1.1.2/24
GE0/0/0
10.0.0.2/24
GE0/0/1
20.1.1.3/24
GE0/0/0
10.0.0.1/24
RTA
RTC
RTB
30.1.2.0/24
[RTA] ip route-static 30.1.2.0 24 20.1.1.3
The next hop of the route to 30.1.2.0/24 is 20.1.1.3, which is not on a directly connected network of RTA. If the IP routing table does not have a route to 20.1.1.3, this static route does not take effect and cannot be installed in the IP routing table.

## Slide 38: Route Recursion (2)
[RTA] ip route-static 30.1.2.0 24 20.1.1.3
[RTA] ip route-static 20.1.1.0 24 10.0.0.2
Recursion
Configure a route to 20.1.1.3, with the next hop pointing to 10.0.0.2 on the directly connected network.
In this way, RTA can recurse the route with the destination 30.1.2.0/24 to the route with the destination 10.0.0.2.
GE0/0/1
20.1.1.2/24
GE0/0/0
10.0.0.2/24
GE0/0/1
20.1.1.3/24
GE0/0/0
10.0.0.1/24
RTA
RTC
RTB
30.1.2.0/24
Destination/Mask | Next Hop | Outbound Interface
30.1.2.0/24 | 20.1.1.3 | GE0/0/0
20.1.1.0/24 | 10.0.0.2 | GE0/0/0
Route Recursion
Equal-Cost Route
Floating Route
Route Summarization

## Slide 39: Equal-Cost Route
When there are equal-cost routes in the IP routing table, a router forwards IP packets to be sent to the destination subnet through all valid outbound interfaces and next hops in the equal-cost routes, achieving load balancing.
10.0.0.0/30
RTA
RTB
GE0/0/0
20.1.1.1/30
GE0/0/1
30.1.1.1/30
GE0/0/1
30.1.1.2/30
GE0/0/0
20.1.1.2/30
Cost=10
Cost=10
RTA's IP routing table
Destination/Mask | Next Hop
10.0.0.0/30 | 20.1.1.2
 | 30.1.1.2
If there are multiple routes to the same destination from the same source, with the same cost, but pointing to different next hops, the routes are installed in the IP routing table as equal-cost routes. Traffic to be sent to the destination will be distributed to these equal-cost routes.
Route Recursion
Equal-Cost Route
Floating Route
Route Summarization

## Slide 40: Floating Route - Basic Concepts
RTB
RTA
RTC
10.1.1.1/30
10.1.2.1/30
10.1.1.2/30
10.1.2.2/30
[RTA] ip route-static 20.0.0.0 30 10.1.1.2
[RTA] ip route-static 20.0.0.0 30 10.1.2.2 preference 70
Configure a floating route on RTA.
Floating Route
Different preferences can be manually configured for static routes. Therefore, you can configure two static routes with the same destination address/mask but different preferences and next hops to implement backup of forwarding paths.
A backup route is known as a floating route, which is used only when the primary route is unavailable. That is, a floating route is installed in the IP routing table only when the next hop of the primary route is unreachable.
20.0.0.0/30
Route Recursion
Equal-Cost Route
Floating Route
Route Summarization

## Slide 41: Floating Route - Example
RTA's IP routing table when the primary link is available
Destined for 20.1.1.0/24
RTB
RTA
RTC
10.1.1.1/30
10.1.2.1/30
10.1.1.2/30
10.1.2.2/30
Destination | Next Hop | Preference
20.0.0.0 | 10.1.1.2 | 60
Destined for 20.1.1.0/24
RTB
RTA
RTC
10.1.1.1/30
10.1.2.1/30
10.1.1.2/30
10.1.2.2/30
Floating Route Switching
20.0.0.0/30
20.0.0.0/30
RTA's IP routing table when the primary link fails
Destination | Next Hop | Preference
20.0.0.0 | 10.1.2.2 | 70
Route Recursion
Equal-Cost Route
Floating Route
Route Summarization
Notes: When the link between RTA and RTB is normal, the two routes to 20.0.0.0/30 are both valid. In this case, RTA compares the preferences of the two routes, which are 60 and 70 respectively. Therefore, the route with the preference value 60 is installed in the IP routing table, and RTA forwards traffic to the next hop 10.1.1.2.
If the link between RTA and RTB is faulty, the next hop 10.1.1.2 is unreachable, which causes the corresponding route invalid. In this case, the backup route to 20.0.0.0/30 is installed in the IP routing table. RTA forwards traffic destined for 20.0.0.1 to the next hop 10.1.2.2.

## Slide 42: CIDR
Classless Inter-Domain Routing (CIDR) uses IP addresses and masks to identify networks and subnets. CIDR replaces the previous addressing architecture of classful network design (such as classes A, B, and C addresses).
CIDR is based on variable length subnet mask (VLSM). CIDR uses prefixes of any lengths to divide the address space with continuous IP addresses. Multiple address segments with continuous prefixes can be summarized into a network, effectively reducing the number of routing entries.
0 | 0 | 0 | 0 | 1 | 1 | 0 | 0
192. | 168.
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
192. | 168.
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 0 | 1
192. | 168.
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 1 | 1 | 0
192. | 168.
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
192.168.12.0/22
192.168.10.0/23
192.168.9.0/21
192.168.14.0/23
192.168.8.0/21
Route Recursion
Equal-Cost Route
Floating Route
Route Summarization

## Slide 43: Background of Route Summarization
RTB's IP routing table
RTA
192.168.1.0/24
192.168.2.0/24
192.168.3.0/24
192.168.4.0/24
192.168.5.0/24
192.168.6.0/24
To route traffic to the directly connected network segments of RTA, RTB must have routes to these network segments. If a static route is manually configured for each network segment, the configuration workload will be heavy and RTB's IP routing table will have a large number of routing entries.
Subnet division and VLSM resolve the problem of address space waste, but also bring a new challenge: increasing routing entries in the IP routing table.
Route summarization can minimize routing entries.
192.168.2.0/24
192.168.1.0/24
192.168.3.0/24
192.168.4.0/24
192.168.5.0/24
192.168.6.0/24
RTB
Route Recursion
Equal-Cost Route
Floating Route
Route Summarization
Notes: On a large-scale network, routers or other routing-capable devices need to maintain a large number of routing entries, which will consume a large amount of device resources. In addition, the IP routing table size is increasing, resulting in a low efficiency of routing entry lookup. Therefore, we need to minimize the size of IP routing tables on routers while ensuring IP reachability between the routers and different network segments. If a network has scientific IP addressing and proper planning, we can achieve this goal by using different methods. A common and effective method is route summarization, which is also known as route aggregation.

## Slide 44: Overview of Route Summarization
RTA
10.1.1.0/24
10.1.2.0/24
...
...
...
10.1.10.0/24
12.1.1.1
RTB
12.1.1.2
[RTA] ip route-static 10.1.0.0 16 12.1.1.2
On RTA, configure static routes to the directly connected network segments 10.1.1.0/24, 10.1.2.0/24, ..., and 10.1.10.0/24 of RTB, with the same next hop. Therefore, these routes can be summarized into one route.
Route summarization is an approach of summarizing routes with the same prefix into one summary route to minimize the IP routing table size and improve device resource usage.
Route summarization uses CIDR to summarize network segments with the same prefix into a single one.
The routes before being summarized are known as specific routes, and the routes created after summarization are known as summarized routes or summary routes.
Route Recursion
Equal-Cost Route
Floating Route
Route Summarization
Notes: To enable RTA to reach remote network segments, we need to configure a specific route to each network segment. In this example, the routes to 10.1.1.0/24, 10.1.2.0/24, and 10.1.3.0/24 have the same next hop, that is, 12.1.1.2. Therefore, we can summarize these routes into a single one.
This effectively reduces the size of RTA's IP routing table.

## Slide 45: Summarization and Calculation
Network address
To summarize routes to multiple continuous network segments into one summary route that just includes these network segments, ensure that the mask length of the summary route is as long as possible.
The key to achieve this is to convert the destination addresses of specific routes into binary numbers and then find out the identical bits in these binary numbers.
192.168.1.0/24
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
192.168.2.0/24
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
192.168.3.0/24
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
192
168
X
0
Host address
192.168.0.0/22
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Route Recursion
Equal-Cost Route
Floating Route
Route Summarization

## Slide 46: Problems Caused by Route Summarization (1)
RTA
10.1.1.0/24
10.1.2.0/24
...
...
...
10.1.10.0/24
12.1.1.1
RTB
12.1.1.2
[RTA] ip route-static 10.1.0.0 16 12.1.1.1
[RTB] ip route-static 0.0.0.0 0 12.1.1.2
Loop
Routing Loop
RTB receives traffic destined for 10.1.20.0/24 and forwards the traffic to RTA according to the default route.
Routes are summarized on RTA. Therefore, RTA forwards the traffic back to RTB according to the summary route to 10.1.0.0/16.
1
2
3
Internet
Route Recursion
Equal-Cost Route
Floating Route
Route Summarization

## Slide 47: Problems Caused by Route Summarization (2)
RTA
10.1.1.0/24
10.1.2.0/24
...
...
...
10.1.10.0/24
12.1.1.1
RTB
12.1.1.2
[RTA] ip route-static 10.1.0.0 16 12.1.1.1
[RTB] ip route-static 0.0.0.0 0 12.1.1.2
Solution for Preventing Routing Loops
Internet
[RTB] ip route-static 10.1.0.0 16 0 NULL0
Configure a route pointing to Null0 on RTB to prevent routing loops when summarizing routes.
Route Recursion
Equal-Cost Route
Floating Route
Route Summarization
Notes: In most cases, both static and dynamic routes need to be associated with an outbound interface. This interface is the egress through which the device is connected to a destination network. The outbound interface in a route can be a physical interface such as a 100M or GE interface, or a logical interface such as a VLANIF or tunnel interface. There is a special interface, that is, Null interface. It has only one interface number, that is, 0. Null0 is a logical interface and is always up. When Null0 is used as the outbound interface in a route, data packets matching this route are discarded, like being dumped into a black-hole. Therefore, such a route is called a black-hole route.

## Slide 48: Accurate Route Summarization (1)
[RTA] ip route-static 172.16.0 16 10.0.0.2
To simplify the configuration, an administrator may configure a static summary route on RTA to allow RTA to reach network segments 172.16.1.0/24 to 172.16.31.0/24 of RTB. However, this summary route also includes the network segments of RTC. As a result, RTA forwards the traffic destined for network segments of RTC to RTB, causing data packet loss. This problem is caused by inaccurate route summarization. To resolve this problem, the summary route must be as accurate as possible; that is, it just covers all specific routes that are to be summarized, with no extra route included.
RTA
RTB
RTC
10.0.0.2
20.0.0.2
172.16.1.0/24
172.16.2.0/24
...
172.16.31.0/24
172.16.32.0/24
172.16.33.0/24
...
172.16.63.0/24
Route Recursion
Equal-Cost Route
Floating Route
Route Summarization

## Slide 49: Accurate Route Summarization (2)
10.1.1.0/24
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
10.1.2.0/24
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
10.1.3.0/24
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
10
1
0
0
/22
ip route-static 10.1.1.0 24 12.1.1.2
ip route-static 10.1.2.0 24 12.1.1.2
ip route-static 10.1.3.0 24 12.1.1.2
ip route-static 10.1.1.0 22 12.1.1.2
Accurately calculate the summarized network address and mask to ensure accurate route summarization.
Route Recursion
Equal-Cost Route
Floating Route
Route Summarization

## Slide 50
How does a router select the optimal route?
How do I configure a floating route?
What is the summary route for routes to 10.1.1.0/24, 10.1.3.0/24, and 10.1.9.0/24?
Notes: The router first compares preferences of routes. The route with the lowest preference value is selected as the optimal route. If the routes have the same preferences, the router compares their metrics. If the routes have the same metric, they are installed in the IP routing table as equal-cost routes.
To configure a floating route, configure a static route with the same destination network segment and mask as the primary route but a different next hop and a larger preference value.
The summary route is 10.1.0.0/20.

## Slide 51
This section presents the basic concepts of routes, how routes instruct routers to forward IP packets, common route attributes, and default routes (special static routes).
In addition, this section describes advanced routing features including route recursion, floating routes, and equal-cost routes, which are widely used on live networks.